## Slide 1
RSP : Robot support package
BSP : Board support package
FreeRtos
AccStepper
Librairie tierce
Servo
Arduino core
ArdOs
nanopb
AccServo
Gpio tools
SerialDriver
Code ARD
Applicative Layer
Strat
Thread
Actuators
Thread
Nav
Detection
Log
Thread
Teleop
Thread
MateCom
Thread
FSM
Yakindu
Legend:
Robot2017
HMI
Spi/SD

## Slide 2
Component | Responsibility / description
SerialDriver | Provide software access to the serial bus.
Spi/SD | Manage Spi bus, read SD cards, manage filesystem.
FreeRtos | Real time safe preemptive operating system.
AccStepper | Convert a stepper motor position command into phase signals.
Servo | Convert a servo position command into a PWM signal.
Gpio | Provide software access to the GPIO banks.
Nanopb | Enable data serialization/deserialization for communication bus.
Teleop Thread | Listen to Dev-PC commands on the programmer serial bus. May be used to manually drive the robot in place of the strategy, or to simulate HW actions.
MateCom Thread | Listen to the other robot.
ArdOs | Provide C++ high level OS abstraction (mutex, signals, “no malloc enforcement”).
Log Thread | Provide a logging message queue so that critical deadlined tasks are not slowed by any serial/file system access. Allow to duplicate logs on several channels.
AccServo | Add trapeze motion profiles to the Servo component.
GpioTools | Add filters and LED controls on the Gpio component.
Robot2017 | Assemble and build object instances of the 2017 robot. Hold all configurations
Strat Thread | Drive the robot during the match.
Actuators Thread | Drive actuators and read captors.
Nav & Detection | Provide robot motion and basic avoidance (anti-collision).