## Slide 1
RSP : Robot support package
BSP : Board support package
FreeRtos
AccStepper
Librairie tierce
Servo
Arduino core
ArdOs
nanopb
AccServo
Gpio tools
SerialDriver
Code ARD
AL : Applicative Layer
Strat
Thread
Actuators
Thread
Nav
Detection
Log
Thread
Teleop
Thread
MateCom
Thread
FSM
Yakindu
Legend:
Robot2017
HMI
Spi/SD

## Slide 2
Component | Responsibility / description
SerialDriver | Provide software access to the serial bus.
Spi/SD | Manage Spi bus, read SD cards, manage filesystem.
FreeRtos | Real time safe preemptive operating system.
AccStepper | Convert a stepper motor position command into phase signals.
Servo | Convert a servo position command into a PWM signal.
Gpio | Provide software access to the GPIO banks.
Nanopb | Enable data serialization/deserialization for communication bus.
Teleop Thread | Listen to Dev-PC commands on the programmer serial bus. May be used to manually drive the robot in place of the strategy, or to simulate HW actions.
MateCom Thread | Listen to the other robot.
ArdOs | Provide C++ high level OS abstraction (mutex, signals, “no malloc enforcement”).
Log Thread | Provide a logging message queue so that critical deadlined tasks are not slowed by any serial/file system access. Allow to duplicate logs on several channels.
AccServo | Add trapeze motion profiles to the Servo component.
GpioTools | Add filters and LED controls on the Gpio component.
Robot2017 | Assemble and build object instances of the 2017 robot. Hold all configurations
Strat Thread | Drive the robot during the match.
Actuators Thread | Drive actuators and read captors.
Nav & Detection | Provide robot motion and basic avoidance (anti-collision).